Chess clock

Use an LCD module to display the time.
That means using a 5V supply.

Use an ATMEGA88P running at 1MHz

Scavenge parts from the previous chess clock:
Use the same end-of-turn, pause and restart buttons
Use second-board pushbutton unit as-is

LCD modules have a 16-pin interface.
2 for backlighting, 3 for power, 3 for control, 8 for data
The LCD modules can be used in a 4-bit mode
That needs 7 pins, but can make do with 6.

6 of the ATMEGA8 pins are used for power and reset, leaving 22.

Need 4 end-of-turn pushbutton inputs.
Need 1 beeper output.

Use timer 1 in fast PWM mode with OCR1A for the TOP value, to toggle OC1A
Only turn on and configure timer 1 when needed for audio

Use timer 2 in fast PWM mode with OCR2A for the TOP value. That permits PWM control of OC2B to have adjustable LED backlight one day.

Pin	Function	Usage	Pin	Function	Usage
1	reset	ICE reset	28	PC5/ADC5/SCL	LCD R/W
2	PD0/RXD	LCD E	27	PC4/ADC4/SDA	LCD RS
3	PD1/TXD	EOT1 PB	26	PC3/ADC3	LCD DB4
4	PD2/INT0	EOT2 PB	25	PC2/ADC2	LCD DB5
5	PD3/INT1/OC2B	LCD Backlight	24	PC1/ADC1	LCD DB6
6	PD4/XCK/T0	Up PB	23	PC0/ADC0	LCD DB7
7	VCC	Power	22	GND	Power
8	GND	Power	21	AREF	Not connected
9	PB6/XTAL1	Turn1 LED	20	AVCC	Power
10	PB7/XTAL2	Turn2 LED	19	PB5/SCK	Copy PB
11	PD5/T1	Turn3 LED	18	PB4/MISO	Pause/mode PB
12	PD6/AIN0	Turn4 LED	17	PB3/MOSI/OC2A	Restart PB
13	PD7/AIN1	EOT3 PB	16	PB2/SS/OC1B	Down PB
14	PB0/ICP	EOT4 PB	15	PB1/OC1A	audio

To conserve power, turn off:
ADC
Analog comparator
Brownout detector
Watchdog timer
Timer0
TWI
SPI
USART